Experimentally Determined Tilt and Bending Moduli of Single-Component Lipid Bilayers

John F Nagle   (nagle@cmu.edu)

Department of Physics, Carnegie Mellon University, Pittsburgh, PA 15213

3/16/2017

Abstract:

Values of the bending modulus KC and the tilt modulus K are reported for single component lipid bilayers.  The lipids studied have the common names DOPC, DMPC, diC22:1PC, SOPC, POPC, diPhyPC, DLPC, DPPC, DHPC and DEPC, listed in the order of number of samples examined.  The experimental method, thus far the only one that measures the tilt modulus of lipid bilayers, first obtains diffuse X-ray scattering data from oriented stacks of bilayers.  The values of the moduli emerge from fitting the data to the accepted tilt-dependent continuum model for the free energy of a single bilayer, further enhanced by interactions between bilayers in the stack.  The results indicate the broad trend that the tilt modulus for these PC lipids is smaller the closer the temperature is to the main transition temperature.  Another trend is that inclusion of tilt raises the value of the bending modulus more for lipids with smaller values of the tilt modulus.  Values of both moduli are compared to recent literature values obtained from simulations and values of the bending modulus are compared to the literature values obtained by other experimental methods.

Key Words:     Mechanical properties of membranes, tilt modulus, bending modulus, diffuse X-ray scattering, lipid bilayers

I.  Introduction

It is widely recognized that an especially important property of biomembranes is their flexibility that allows for biological function.  For this, the bending modulus KC is the most important measure of resistance to bending.   Along with spontaneous curvature and the Gaussian modulus, it provides the basic, lowest-order, long length scale description of the curvature properties of membranes, as embodied in the Helfrich-Canham theory (Helfrich, 1973), which is the simplest theoretical framework that incorporates the bending modulus. For symmetric lipid bilayers of fixed topology this is a one parameter continuum theory in which the curvature energy is proportional to the bending modulus, which is lipid specific, times the membrane curvature squared.  Although a recent modification has recently been proposed for gel phase bilayers (Diggins et al., 2015), the Helfrich-Canham (HC) theory is generally deemed valid for the fluid phase at long length scales.

In contrast, simulations have made it clear that the HC theory is not valid at shorter length scales (Goetz et al., 1999, Lindahl and Edholm, 2000).  A growing consensus is that the continuum theory can be significantly improved by including a molecular tilt degree of freedom, even for the fluid phase above the chain melting phase transition and (Hamm and Kozlov, 2000) (HK) proposed such a theory.  It has long been known that chains in phosphatidylcholine lipids undergo cooperative, spontaneous tilt in the gel phase.  Of course, the average tilt is zero in the fluid phase, but individual chains may tilt locally.  The HK theory incorporates this with a tilt field and an appropriate addition to the theoretical free energy.  Importantly for biological relevance, it was shown (Kozlovsky and Kozlov, 2002) that the HK theory alleviated a major theoretical concern, namely, that the HC theory had predicted an impossibly large activation energy for the fusion of membranes (Siegel, 1999).  Subsequently, it was shown that the HK theory also quantitatively accounts for the observed deviations in the simulated fluctuation spectra (May et al., 2007).   Further development of the tilt theory has been made (Watson et al., 2011), including methods for extracting both the tilt modulus K and the bending modulus KC from simulations (Watson et al., 2012); this further theory has also passed an additional recent test regarding how the length of the hydrocarbon tails depends on the actual tilt of individual chains (Kopelevich and Nagle, 2015).

While it has been clear that incorporating both bending and tilt is important for theory and simulations, experimentally measuring the accompanying tilt modulus has lagged.  It appears to be impossible to measure K by the classical methods that have been developed to measure KC because those measurements are on length scales in the plane of the membrane that are too large to detect tilt (Nagle et al., 2015).  In contrast, diffuse x-ray scattering obtains transverse flexibility information at a shorter in-plane length scale.  Recently, it has been shown how to obtain the value of the tilt modulus, as well as of the bending modulus, from diffuse x-ray scattering, and results have been presented for DOPC bilayers (Jablin et al., 2014).  At this time, this is the only experimental method that has been advanced for obtaining values of the tilt modulus of lipid bilayers.

Diffuse x-ray scattering data for many lipid bilayers have been obtained in this lab since 2003.  These data had previously been analyzed based on the HC theory and values of KC had been reported in a series of papers, each of which focused on one or a few lipids or on lipid bilayers with an additive.  The present paper reports the results of using the tilt-dependent theory to re-analyze some of those data.  All of the results in this paper are for single component lipid bilayers in the fluid phase, mostly at T=30 C except for two lipids that have higher phase transition temperatures.  The effect of temperature and effects of additives, e.g. cholesterol, will be presented elsewhere.  In addition to providing the first experimental values of the tilt modulus K for many bilayers in addition to DOPC, this study reports revised x-ray values for the bending modulus KC that are then compared to literature values obtained by classical methods.

II.  Experimental

All the lipids studied had been obtained from Avanti Polar Lipids (Alabaster, Alabama), 1,2-dilauroyl-sn-glycero-3-phosphocholine (DLPC), 1,2-dimyristoyl-sn-glycero-3-phosphocholine (DMPC), 1,2-dipalmitoyl-sn-glycero-3-phosphocholine (DPPC), 1-palmitoyl-2-oleoyl-sn-glycero-3-phosphocholine (POPC), 1-stearoyl-2-oleoyl-sn-glycero-3-phosphocholine (SOPC), 1,2-dioleoyl-sn-glycero-3-phosphocholine (DOPC), 1,2-dierucoyl-sn-glycero-3-phosphocholine (diC22:1PC), 1,2-dielaidoyl-sn-glycero-3-phosphocholine (DEPC), 1,2-diphytanoyl-sn-glycero-3-phosphocholine (diPhyPC), 1,2-di-O-hexadecyl-sn-glycero-3-phosphocholine (DHPC).  Oriented stacks consisting of approximately 2000 bilayers had been prepared using the rock-and-roll method  (Tristram-Nagle, 2007).

The method for obtaining diffuse x-ray scattering data has been previously described (Kucerka et al., 2005a, Liu, 2003, Jablin, 2015).  Briefly, oriented stacks of approximately 2000 bilayers supported on a flat Si substrate are rotated in the x-ray beam to provide cumulative intensity for all incident angles on a CCD detector.  An example of the CCD image is shown in Fig. 1.  All data re-analyzed in this paper had been obtained at the CHESS synchrotron.

Fig. 1.  Rendition of the background subtracted, symmetrized, scattering intensity with an overlay of the fitted residuals in the two rectangles lightly outlined in blue.  The largest intensities (above 4000) are shown by green pixels.  Red pixels indicate negative values.  The diffuse scattering is shown by a grayscale from black (zero) to full white (above 200).  The strongly attenuated direct beam is near the small white dot located near the bottom at pixel  (500,80).  Less strongly attenuated are the h=1 order at (500,185) and the h=2 order at (500,290) near which there are three green spots due to its unattenuated tails; both these orders appear in what we define as the first lobe of diffuse scattering.  The second lobe contains two green regions at larger values of pz; these are smeared h=3 and h=4 orders.  The data were fit in the two rectangular boxes outlined in blue and the portrayed intensities in those boxes are the residuals to the fit, with values typically less than 1% of the average intensity.

The mechanical moduli were evaluated using a fitting program (NFIT, (Liu, 2003, Jablin, 2015) ) that obtained the smallest 2 in an area of the CCD that comprised approximately 50000 CCD pixels as shown in Fig. 1; in reciprocal space this generally ranged from about 0.2 to 0.6 Å-1 in the vertical direction along the average bilayer normal and from about 0.01 to 0.3 Å-1 in the horizontal in-plane direction.  There are many input parameters in NFIT.  These include obvious experimental conditions, as well as less obvious ones like beam divergence and energy dispersion.  Input parameters also include details of the sample geometry and the repeat spacing (D) of bilayers in the stack.  A full list of input parameters is provided in Supplementary Material along with their uncertainties and how much those uncertainties affect the values of the bending and tilt moduli obtained from NFIT.  The uncertainties in most input parameters affect the values of the moduli relatively little compared to differences obtained from nominally identical samples.  An exception is that two different treatments of the background gave differences in KC by about 10% for some lipids, and even larger differences for K also occurred.  Reported values in this paper are averages from the two treatments.  The tilt-dependent analysis has been described briefly (Jablin et al., 2014) and also in much more detail (Jablin, 2015).

Typically, data were obtained for several values of the lamellar repeat D spacing of the stack of bilayers; D varied as the hydration level varied.  However, the results in this report only include the best exposure from one D spacing per sample because the moduli, in accordance with theory, do not depend systematically upon D, as was previously shown for the tilt-independent bending modulus (Pan et al., 2008).  (The analysis also must fit a bulk B modulus.  The value of B clearly depends upon D (Pan et al., 2008) because B involves the interaction between neighboring bilayers which becomes exponentially stronger as D decreases (Petrache et al., 1998).  Interestingly, the value of B was very nearly the same for a given D whether the tilt-dependent or the tilt-independent analysis is used.)  The criteria for the chosen exposure for each sample were (i) the D spacing was large enough to have substantial diffuse scattering for accurate analysis, (ii) the sample was not noticeably flooded with excess water which can occur when trying to achieve maximal hydration, and (iii) choosing a location on the sample where it was well oriented.  It was advantageous to hydrate samples to near their fully hydrated level, defined as the value of D obtained in unoriented multilamellar vesicles (MLV) dispersed in excess water, because there was then more diffuse scattering; however, the other criteria sometimes motivated reporting results from a smaller value of D.

III.  Results

Table 1 presents the main results of this paper.  Column 1 of Table 1 lists the single component lipids for which diffuse x-ray scattering data are available.  Column 2 lists the number of independent samples.  The different samples of most lipids were examined on different synchrotron runs.  A notable exception was that 14 samples of DOPC were examined on the same run; these had the same standard deviation in the values of the moduli as samples from different runs, indicating that sample variation, not experimental condition, was primarily correlated with uncertainties in the values of the moduli. The third column shows the temperature.  The next column gives the range of lamellar repeat D spacings analyzed for the different samples of each lipid.  Although the maximum D in this range is typically close to the fully hydrated value, it is smaller for some lipids.

| Lipid | N samples | T (°C) | D Å | K mN/m | KCtd/kT | KCti/kT | KCtd/KCti | KClit/kT | KCti/KClit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DOPC | 26 | 30 | 60.9-64.9 | 89±4 | 19.4±0.7 | 16.3±0.5 | 1.19 | 18.2±2.7a | 0.89 |
| DMPC | 13 | 30 | 60.6-63.2 | 44±2 | 24.6±1.0 | 15.6±0.6 | 1.58 | 15.8±2.4a | 0.99 |
| diC22:1PC | 4 | 30 | 66.9-69.0 | 58±5 | 46.2±1.2 | 28.3±1.3 | 1.63 | 30.6±1.6a | 0.93 |
| POPC | 4 | 30 | 62.0-64.3 | 73±12 | 25.7±2.1 | 19.2±1.2 | 1.34 | 20.3b | 0.95 |
| SOPC | 3 | 30 | 62.9-66.9 | 60±5 | 24.6±2.9 | 18.5±1.9 | 1.33 | 21.1±1.6a | 0.86 |
| diPhyPC | 3 | 30 | 61.8-63.4 | 109±18 | 17.4±1.8 | 14.9±1.3 | 1.17 | 12.4±1.5c | 1.20 |
| DLPC | 2 | 30 | 61.2-62.9 | 55±5 | 20.4±1.4 | 14.3±0.7 | 1.43 | 13.2d | 1.09 |
| DPPC | 2 | 50 | 64-67 | 43±4 | 27.5±3.4 | 18.3±3.1 | 1.50 | 15.0±1.6e | 1.22 |
| DHPC (ether) | 1 | 48 | 66.5 | 38±16 | 30.6±4.5 | 19.1±3.1 | 1.61 | 12.4±1.7e | 1.53 |
| DEPC trans18:1 | 1 | 30 | 71 | 57±16 | 21.2±4.5 | 17.0±3.1 | 1.25 | - | - |

Table 1.    Mean moduli for the N samples of the lipid bilayers studied at the shown temperature T.   The tilt-dependent bending modulus KCtd and the tilt-independent bending modulus KCti are given in units of kT and their ratio is shown in the third to last column.  Uncertainties in the moduli are the standard error of the mean for N>1 and for N=1 they were estimated from standard deviations of other lipids.  Previously published results for the tilt-independent bending modulus are shown in the penultimate column as KClit and the ratio with the KCti obtained in this paper is shown in the last column.  References are a(Nagle, 2013), b(Kucerka et al., 2005b), c(Tristram-Nagle et al., 2010), d(Kucerka et al., 2005a), e (Guler et al., 2009).

The column labeled K in Table 1 shows the mean values of the tilt modulus weighted for the N samples for each lipid. (Most weights were unity, but a few less optimal samples were assigned smaller weights.)  The column labeled KCtd in Table 1 shows the mean value of the bending modulus obtained by allowing the tilt modulus Kto fit; this is called the tilt-dependent (td) value of KC.  The column labeled KCti in Table 1 gives the value of the bending modulus obtained by fixing Kto a large value; this suppresses consideration of the tilt degree of freedom so these are called the tilt-independent (ti) values of KC.  The uncertainties shown in Table 1 are the standard errors of the mean for those lipids for which we had more than one sample.  The uncertainty assigned to lipids for which there was only one sample was set close to the maximum standard deviation found for the other lipids.  The standard deviations obtained from all samples of the same lipid can be thought of as arising from two sources.  First, is the uncertainty obtained from the systematic fitting protocol.  This is rather small compared to the second uncertainty which comes from different samples of the same lipid.  We have tried to identify an experimental cause for this sample variation and to eliminate it, but without success.  Figure 2 shows variations in the values of KCtd and Kfor all DOPC samples.

Figure 2.  Results for the tilt Kand bending KCtd moduli for the 26 samples of DOPC.

The third to last column in Table 1 shows the ratio of the average tilt-dependent bending modulus KCtd to the average tilt-independent bending modulus KCti.  Uncertainties are not assigned to these ratios because the two values are correlated to an uncertain degree.  Figure 3 plots this ratio versus the tilt modulus for all our studied lipids.  The results for the most studied lipid bilayers indicate that the smaller average tilt modulus of DMPC increases the tilt-dependent bending modulus KCtd more compared to the bending tilt-independent modulus KCti than does the larger average tilt modulus of DOPC.  Of the other lipids, only the deviation of C22:1 is substantially inconsistent with the general trend indicated in Fig. 3.

Figure 3.  Ratio of tilt-dependent bending modulus KCtd to tilt-independent bending modulus KCti versus tilt modulus K for the 10 lipids studied.  The dash-dot line suggests a correlation.

The next to last column in Table 1 shows previously published values of tilt-independent KC from this lab and the last column shows the ratio with the new tilt-independent values.  Some deviations from unity occur partly because additional samples are now averaged.  Other differences may be attributed to the new NFIT program and the associated protocol that treat coherence and domain sizes somewhat differently (Jablin, 2015).

Figure 4 shows the values of the tilt modulus versus the difference T between the measured temperature and temperature TM  of the main transition from the fluid phase into the rippled or gel phase.  As in Fig. 3, there is a strong difference for our most studied DOPC and DMPC lipids.  The dot-dash line in Fig. 4 indicates a strong correlation for all the lipids with phosphocholine (PC) headgroups.  This leads one to predict that the tilt modulus should decrease as the main transition is approached for each lipid.   A subsequent paper will present data that confirm this prediction for DMPC.

Figure 4.  Tilt modulus K versus temperature difference T between the experimental temperature and the main chain melting transition temperature TM of each of 9 lipids with known TM.  A correlation is suggested by the dash-dot line.

IV.  Discussion

There is an important connection between the tilt modulus and the bending modulus regarding the overall flexibility of membranes.  Inclusion of tilt in the tilt-dependent analysis always increases the value of KCtd compared to the tilt-independent value KCti, as shown in the third to last column of Table I.  This is expected because a reduction in either modulus softens a membrane overall.  The tilt-independent fit assumes an infinite value of K. Allowing K to fit in the tilt-dependent analysis therefore increases KC in order to achieve the same overall softness.  (However, note that, compared to KC, K softens preferentially at smaller length scales – otherwise, separate values for the two moduli could not be extracted from the experimental data and the goodness of the fit would not be better for the tilt-dependent fit.)  It then follows that the increase in KC should generally be greater for a lipid that has a smaller K than for one with a larger K.  Figure 3 generally confirms this, especially for DOPC and DMPC for which we have the best statistics.  Figure 3 shows that the ratio of tilt-independent to tilt-dependent values of KC for other lipids generally follows the trend, with the most notable exception being C22:1 which forms the thickest bilayers (Kucerka et al., 2005b).

As a tilt degree of freedom makes membranes more flexible at the short length scale appropriate for important properties like fusion, it should be of interest to learn what affects the tilt modulus.  Unexpectedly, the strongest correlation found here for the PC lipids is the proximity T to the main fluid disordered to ordered phase transition temperature shown in Fig. 4.  This is reminiscent of early biomembrane studies that reported optimal growth of various organisms occurred above but near the chain melting transition (Steim et al., 1969), although one should not push this connection too far as biomembranes are complex mixtures of many lipids and proteins.    The fraction of unsaturated double bonds in the hydrocarbon chains would have seemed, a priori, to provide a useful correlation, and it does, in so far as double bonds lower the phase transition temperature.  However, both C22:1 and DOPC have higher fractions of double bonds than SOPC and POPC, but of these four lipids, the former pair have widely different values of K and the latter pair have intermediate values at T=30°C.   One might also have guessed a priori that the tilt modulus would be correlated with the thickness of the bilayer, but our best studied DOPC and DMPC have nearly equal thicknesses (Nagle and Tristram-Nagle, 2000), but much different values of KThe result that Kis strongly correlated with T leads one to expect that the tilt modulus should decrease as the main transition is approached for each lipid; a subsequent paper will report results that strongly confirm this expectation for DMPC.

The idea that the tilt modulus increases with increasing temperature seems counter-intuitive, so it is reassuring that there is a theoretical equation that predicts the same direction (Watson et al., 2011),

K = 2ow – B/A2 ,						(1)

where ow is oil-water surface tension (typically ~50 mN/m) and  B/A2 was subtracted to take into account the repulsive interaction between headgroups, where A is the area/lipid and B is a positive constant.  According to Eq. (1), K would decrease with increasing temperature because area A increases.  It is interesting to see whether Eq. (1) agrees with our data.  Figure 5 shows values of K when B is fixed to provide agreement with the experimental values for DMPC and experimental values of A are used.  Disagreement for DOPC is especially strong.  Because the repulsive interaction between headgroups becomes infinite for A smaller than the A ~ 48Å2 that occurs in the gel phase of PC lipids (Tristram-Nagle et al., 2002), Fig. 5 also shows values of K for a modified formula where A is replaced by (A-48Å2).   Disagreement is then alleviated for DOPC and DPhyPC, although agreement is poorer for three other lipids.  Neither equation correlates as well as Fig. 4.

Figure 5.  Estimates of tilt modulus from Eq. 1 (red squares) and from a modified equation (blue circles) compared to experimental values.  The solid line represents perfect agreement.  References for experimental values for the areas A are in the caption to Table 1.

Table 2 compares values of the moduli from recent atomistic simulations with X-ray values.  Three of the papers used the analysis method developed by Brown’s group (Watson et al., 2012).  An exception (Wang and Deserno, 2016) analyzed membrane buckling.  For DMPC the two latest simulations agree well with each other (especially when the temperature difference is considered as both moduli rapidly decrease with decreasing temperature in this range), and there is satisfactory agreement with the X-ray results.  For DOPC the X-ray values are significantly larger for Kand significantly smaller for KC.  An a prior reconciliation might be based on Fig. 3, which shows that, for different lipids, a smaller average Kincreases KC more.  However, Fig. 2 shows that there is no correlation between Kand KC for individual samples of DOPC.  Another reconciliation of the DOPC values could be based on the temperature difference between the simulations and the experiments.  Indeed, there are DOPC X-ray data at 15oC and 45oC (Pan et al., 2008) that have been reanalyzed, and interpolation to T=25oC gives values 6% smaller for Kand 6% larger for KC.  While this is in the right direction, it falls short, only decreasing Kto 84 mN/m and increasing KC/kT to 20.6.  It might also be noted that K( 80 mN/m can be gleaned (Nagle et al., 2015) from a real space simulation analysis (Khelashvili and Harries, 2013).   For DPPC and POPC, the X-ray uncertainties for Kare quite large, so there is no disagreement with simulations in Table 2.  The X-ray value for KC for DPPC is a bit smaller, like DMPC.  For POPC the difference divided by the average is 0.25, roughly midway between the similar normalized difference for DMPC (0.15)and DOPC (0.39), suggesting that chain unsaturation may be involved.   It may also be noted that the supplementary material of (Levine et al., 2014) report 18% differences Kthat depend upon how the headgroup end of the molecular tilt was defined; possibly larger differences might occur if the tail end of chains were reconsidered as was done for DMPC only by (Wang and Deserno, 2016), and this might alleviate the discrepancy for lipids with unsaturated chains.  In contrast to simulations, the x-ray analysis is based only upon the continuum model which is impervious to such molecular distinctions, so differences with simulation results due to atomistic tilt definition should be explored further by simulators.

| Lipid | Method | T (oC) | K (mN/m) | KC/kT | Reference |
| --- | --- | --- | --- | --- | --- |
| DMPC | UA | 27 | 56 | 39 | (Watson et al., 2012) |
|  | UA/buckles | 27 | 39±2 | 24.9±1.0 | (Wang and Deserno, 2016) |
|  | CH36 | 30 | 40.2 | 29.21.2 | (Venable et al., 2015) |
|  | X-ray | 30 | 43±2 | 25.1±1.0 | This paper |
| DOPC | CH36 | 24.9 | 66±2 | 27.70.7 | (Levine et al., 2014) |
|  | CH36 | 25 | 64.0 | 28.7±1.0 | (Venable et al., 2015) |
|  | X-ray | 30 | 95±7 | 19.8±1.4 | Jablin et al., 2014 |
|  | X-ray | 30 | 89±4 | 19.4±0.7 | This paper |
|  | X-ray | 25 | 84 | 20.6 | Using (Pan et al., 2008) |
| DPPC | CH36 | 50 | 49±2 | 35.0±1.1 | (Levine et al., 2014) |
|  | CH36 | 50 | 48.8 | 35.4±0.9 | (Venable et al., 2015) |
|  | X-ray | 50 | 44±16 | 28.8±4.5 | This paper |
| POPC | CH36 | 30 | 55.2 | 31.6±1.0 | (Venable et al., 2015) |
|  | X-ray | 30 | 69±17 | 24.6±2.6 | This paper |

Table 2.  Comparison of the values of the tilt-dependent X-ray moduli with those from simulations, where UA connotes united atom and CH36 connotes version 36 of CHARMM.

Values of the tilt-independent X-ray bending modulus KC have previously been compared to literature values obtained from giant unilamellar vesicles using the classical shape analysis (SA) or aspiration pipette membrane mechanics (MM) (Nagle, 2013).  Figure 3 emphasizes that the X-ray values are now larger when the tilt-dependent analysis is employed. Table 3 enables a comparison of these new values to literature values obtained using other methods.   Previously, the tilt-independent X-ray values of KC had agreed with the earliest MM values (Rawicz et al., 2000).  The new X-ray values still agree well for DOPC and borderline well for SOPC, but there are now large differences for DMPC and diC22:1PC.  A few MM results for SOPC from other labs continue to be larger even than the new tilt-dependent X-ray results in Table 3.  The SA values of KC tend to be larger than the new X-ray values as indicated in the last column in Table 3 which shows the ratios of those values.  Previously, using the tilt-dependent X-ray values the ratio was much larger for DMPC than for DOPC.  Now, the ratios in Table 3 appear not to depend significantly upon the lipid.   It should be reiterated that the SA method is definitely not affected by tilt and, while the MM method could be marginally affected by tilt as it spans many decades of length scales, only the shortest decade is affected by tilt (Nagle et al., 2015), so other explanations have to be sought for residual systematic differences with x-ray results.   One obvious difference is that the classical methods study GUV sample whereas x-ray samples are multilamellar arrays which have interactions between adjacent bilayers which are accounted for by the bulk B modulus.  Although this is only a harmonic approximation, it is consistent with the corresponding level of approximation in the HK single membrane continuum model.

| Method Lipid | X-ray | MM | SA | Tethers | SA/ X-ray |
| --- | --- | --- | --- | --- | --- |
| DOPC | 19.4±0.7 | 19.1±2.2a | 26.5±2.7d 24±2e | 16±2j 23±5k | 1.37±0.18 1.23±0.14 |
| SOPC | 24.6±2.9 | 20.2±1.3a 30±1.6b 36.9±1.2c | 30.4±1.7b,f 29.4±6.1g 37.9±0.8h | 26.8±1.8l | 1.24±0.19 1.20±0.36 1.54±0.15 |
| DMPC | 25.1±1.0 | 13.4±1.4a | 31.1±1.9i |  | 1.24±0.12 |
| diC22:1PC | 46.2±1.2 | 27.3±3.4a |  |  |  |

Table 3.  KC/kT values of the bending modulus obtained for some single component bilayers using the new tilt-dependent X-ray method compared to literature values obtained using micromechanical manipulation (MM), shape analysis (SA) and tethers.  The references are a (Rawicz et al., 2000), b(Vitkova et al., 2006), c(Henriksen and Ipsen, 2004), d(Gracia et al., 2010), e(Shchelokovskyy et al., 2011), f(Meleard et al., 1998), g(Pecreaux et al., 2004), h(Henriksen and Ipsen, 2002), i(Meleard et al., 1997), j(Sorre et al., 2009), k(Tian et al., 2009) and l(Heinrich and Waugh, 1996).  Literature values have been adjusted to 30°C (Nagle, 2013).

Many researchers interested only in the overall flexibility of a membrane may not be prepared to consider both a bending modulus and now a tilt modulus.  In that case, the older tilt-independent X-ray values would actually give more appropriate measures of overall flexibility in the sense that they represent a kind of average softness due to the true tilt-dependent bending modulus and the tilt modulus.  However, even the tilt-independent values of the bending modulus are too large to overcome the energy crisis for the stalk model of membrane fusion (Siegel, 1999), so both moduli should be considered. In this regard, it is interesting to compare our two best studied lipids.  DMPC and DOPC have nearly the same thickness (Nagle and Tristram-Nagle, 2000) and Table 1 indicates only slightly larger tilt-independent values of KCti for DOPC, suggesting that there should not be much difference in bilayer properties that depend upon bending.  However, the tilt-dependent results for KCtd indicate that DMPC should be stiffer than DOPC for properties that depend upon bending at large length scales and less stiff than DOPC for smaller length scale properties that depend upon the tilt modulus.

Acknowledgements:  I thank former students, postdocs, researchers and collaborators, too numerous to name individually, who participated in the collection of the data that were previously published using the tilt-independent analysis.  Special thanks are due to Michael Jablin for having persevered in the development of the tilt-dependent analysis and software used in this work.  I thank Dmitry Kopelevich for motivating Figure 5, and Stephanie Tristram-Nagle and Fernando Dupuy for helpful discussion.

Bibliography

DIGGINS, P., MCDARGH, Z. A. & DESERNO, M. 2015. Curvature Softening and Negative Compressibility of Gel-Phase Lipid Membranes. Journal of the American Chemical Society, 137, 12752-12755.

GOETZ, R., GOMPPER, G. & LIPOWSKY, R. 1999. Mobility and elasticity of self-assembled membranes. Physical Review Letters, 82, 221-224.

GRACIA, R. S., BEZLYEPKINA, N., KNORR, R. L., LIPOWSKY, R. & DIMOVA, R. 2010. Effect of cholesterol on the rigidity of saturated and unsaturated membranes: fluctuation and electrodeformation analysis of giant vesicles. Soft Matter, 6, 1472-1482.

GULER, S. D., GHOSH, D. D., PAN, J. J., MATHAI, J. C., ZEIDEL, M. L., NAGLE, J. F. & TRISTRAM-NAGLE, S. 2009. Effects of ether vs. ester linkage on lipid bilayer structure and water permeability. Chemistry and Physics of Lipids, 160, 33-44.

HAMM, M. & KOZLOV, M. M. 2000. Elastic energy of tilt and bending of fluid membranes. European Physical Journal E, 3, 323-335.

HEINRICH, V. & WAUGH, R. E. 1996. A piconewton force transducer and its application to measurement of the bending stiffness of phospholipid membranes. Annals of Biomedical Engineering, 24, 595-605.

HELFRICH, W. 1973. Elastic Properties of Lipid Bilayers - Theory and Possible Experiments. Zeitschrift Fur Naturforschung C-a Journal of Biosciences, C 28, 693-703.

HENRIKSEN, J. R. & IPSEN, J. H. 2002. Thermal undulations of quasi-spherical vesicles stabilized by gravity. European Physical Journal E, 9, 365-374.

HENRIKSEN, J. R. & IPSEN, J. H. 2004. Measurement of membrane elasticity by micro-pipette aspiration. European Physical Journal E, 14, 149-167.

JABLIN, M. S. 2015. Tilt-Dependent Analysis of Diffuse X-ray Scattering from Oriented Stacks of fluid Phase Lipid Bilayers. Dissertation, Carnegie Mellon University, 257.

JABLIN, M. S., AKABORI, K. & NAGLE, J. F. 2014. Experimental Support for Tilt-Dependent Theory of Biomembrane Mechanics. Physical Review Letters, 113, 248102 (1-5).

KHELASHVILI, G. & HARRIES, D. 2013. How Cholesterol Tilt Modulates the Mechanical Properties of Saturated and Unsaturated Lipid Membranes. Journal of Physical Chemistry B, 117, 2411-2421.

KOPELEVICH, D. I. & NAGLE, J. F. 2015. Correlation between length and tilt of lipid tails. Journal of Chemical Physics, 143, 154702(1-8).

KOZLOVSKY, Y. & KOZLOV, M. M. 2002. Stalk model of membrane fusion: Solution of energy crisis. Biophysical Journal, 82, 882-895.

KUCERKA, N., LIU, Y. F., CHU, N. J., PETRACHE, H. I., TRISTRAM-NAGLE, S. T. & NAGLE, J. F. 2005a. Structure of fully hydrated fluid phase DMPC and DLPC lipid bilayers using X-ray scattering from oriented multilamellar arrays and from unilamellar vesicles. Biophysical Journal, 88, 2626-2637.

KUCERKA, N., TRISTRAM-NAGLE, S. & NAGLE, J. F. 2005b. Structure of fully hydrated fluid phase lipid bilayers with monounsaturated chains. Journal of Membrane Biology, 208, 193-202.

LEVINE, Z. A., VENABLE, R. M., WATSON, M. C., LERNER, M. G., SHEA, J. E., PASTOR, R. W. & BROWN, F. L. H. 2014. Determination of Biomembrane Bending Moduli in Fully Atomistic Simulations. Journal of the American Chemical Society, 136, 13582-13585.

LINDAHL, E. & EDHOLM, O. 2000. Mesoscopic undulations and thickness fluctuations in lipid bilayers from molecular dynamics simulations. Biophysical Journal, 79, 426-433.

LIU, Y.-F. 2003. New method to obtain structure of biomembranes using diffuse x-ray scattering: Application to fluid phase DOPC lipid bilayers. Dissertation, Carnegie Mellon University, http://lipid.phys.cmu.edu, 1-128.

MAY, E. R., NARANG, A. & KOPELEVICH, D. I. 2007. Role of molecular tilt in thermal fluctuations of lipid membranes. Physical Review E, 76, 021913(1-6).

MELEARD, P., GERBEAUD, C., BARDUSCO, P., JEANDAINE, N., MITOV, M. D. & FERNANDEZ-PUENTE, L. 1998. Mechanical properties of model membranes studied from shape transformations of giant vesicles. Biochimie, 80, 401-413.

MELEARD, P., GERBEAUD, C., POTT, T., FERNANDEZPUENTE, L., BIVAS, I., MITOV, M. D., DUFOURCQ, J. & BOTHOREL, P. 1997. Bending elasticities of model membranes: Influences of temperature and sterol content. Biophysical Journal, 72, 2616-2629.

NAGLE, J. F. 2013. Introductory Lecture: Basic quantities in model biomembranes. Faraday Discussions, 161, 11-29.

NAGLE, J. F., JABLIN, M. S., TRISTRAM-NAGLE, S. & AKABORI, K. 2015. What are the true values of the bending modulus of simple lipid bilayers? Chemistry and Physics of Lipids, 185, 3-10.

NAGLE, J. F. & TRISTRAM-NAGLE, S. 2000. Structure of lipid bilayers. Biochimica Et Biophysica Acta-Reviews on Biomembranes, 1469, 159-195.

PAN, J. J., TRISTRAM-NAGLE, S., KUCERKA, N. & NAGLE, J. F. 2008. Temperature dependence of structure, bending rigidity, and bilayer interactions of dioleoylphosphatidylcholine bilayers. Biophysical Journal, 94, 117-124.

PECREAUX, J., DOBEREINER, H. G., PROST, J., JOANNY, J. F. & BASSEREAU, P. 2004. Refined contour analysis of giant unilamellar vesicles. European Physical Journal E, 13, 277-290.

PETRACHE, H. I., GOULIAEV, N., TRISTRAM-NAGLE, S., ZHANG, R. T., SUTER, R. M. & NAGLE, J. F. 1998. Interbilayer interactions from high-resolution x-ray scattering. Physical Review E, 57, 7014-7024.

RAWICZ, W., OLBRICH, K. C., MCINTOSH, T., NEEDHAM, D. & EVANS, E. 2000. Effect of chain length and unsaturation on elasticity of lipid bilayers. Biophysical Journal, 79, 328-339.

SHCHELOKOVSKYY, P., TRISTRAM-NAGLE, S. & DIMOVA, R. 2011. Effect of the HIV-1 fusion peptide on the mechanical properties and leaflet coupling of lipid bilayers. New Journal of Physics, 13, 025004.

SIEGEL, D. P. 1999. The modified stalk mechanism of lamellar/inverted phase transitions and its implications for membrane fusion. Biophysical Journal, 76, 291-313.

SORRE, B., CALLAN-JONES, A., MANNEVILLE, J. B., NASSOY, P., JOANNY, J. F., PROST, J., GOUD, B. & BASSEREAU, P. 2009. Curvature-driven lipid sorting needs proximity to a demixing point and is aided by proteins. Proceedings of the National Academy of Sciences of the United States of America, 106, 5622-5626.

STEIM, J. M., TOURTELL.ME, REINERT, J. C., MCELHANE.RN & RADER, R. L. 1969. Calorimetric Evidence for Liquid-Crystalline State of Lipids in a Biomembrane. Proceedings of the National Academy of Sciences of the United States of America, 63, 104-&.

TIAN, A. W., CAPRARO, B. R., ESPOSITO, C. & BAUMGART, T. 2009. Bending Stiffness Depends on Curvature of Ternary Lipid Mixture Tubular Membranes. Biophysical Journal, 97, 1636-1646.

TRISTRAM-NAGLE, S. 2007. Preparation of Oriented, Fully Hydrated Lipid Samples for Structure Determination Using X-Ray Scattering, Totowa, NJ, Humana Press.

TRISTRAM-NAGLE, S., KIM, D. J., AKHUNZADA, N., KUCERKA, N., MATHAI, J. C., KATSARAS, J., ZEIDEL, M. & NAGLE, J. F. 2010. Structure and water permeability of fully hydrated diphytanoylPC. Chemistry and Physics of Lipids, 163, 630-637.

TRISTRAM-NAGLE, S., LIU, Y. F., LEGLEITER, J. & NAGLE, J. F. 2002. Structure of gel phase DMPC determined by X-ray diffraction. Biophysical Journal, 83, 3324-3335.

VENABLE, R. M., BROWN, F. L. H. & PASTOR, R. W. 2015. Mechanical properties of lipid bilayers from molecular dynamics simulation. Chemistry and Physics of Lipids, 192, 60-74.

VITKOVA, V., GENOVA, J., MITOV, M. D. & BIVAS, I. 2006. Sugars in the aqueous phase change the mechanical properties of lipid mono- and bilayers. Molecular Crystals and Liquid Crystals, 449, 95-106.

WANG, X. & DESERNO, M. 2016. Determining the Lipid Tilt Modulus by Simulating Membrane Buckles. Journal of Physical Chemistry B, 120, 6061-6073.

WATSON, M. C., BRANDT, E. G., WELCH, A. J. & BROWN, F. L. H. 2012. Determining biomembrane bending rigidities from simulations of modest size. Physical Review Letters, 109, 028102(1-5).

WATSON, M. C., PENEV, E. S., WELCH, P. M. & BROWN, F. L. H. 2011. Thermal fluctuations in shape, thickness, and molecular orientation in lipid bilayers. Journal of Chemical Physics, 135, 244701(1-22).